## Slide 1
Practical Investigation into Safe Reinforcement
Learning with Autonomous Drive
Tao Sun
04/29/2020

## Slide 2
Background
State of the Art Methods
Implementation and Results
Summary

## Slide 3
Background – Reinforcement Learning (RL)
Reinforcement Learning at Deep Learning Age
  Popular in Atari Games, Go Games, Robotics, etc
  Still Limited Practice in Safety-Critical Applications
    Autonomous Drive, Datacenter Cooling, etc
    Unsafe exploration at the initial stage of RL algorithms
    Serious outcomes might be (e.g. car accidents)
Mnih et al. Nature, 2015 Silver et al. Nature, 2016 Kober et al. IJRR, 2013

## Slide 4
Safe Model-based RL [Berkenkamp et al. NIPS, 2017]
  Theoretical results for stability guarantee based on Lyapunov function
  Need prior knowledge about the physical system (model-based)
  Required Lipschitz continuity conditions might not always true
Constrained Policy Optimization [Achiam et al. ICML, 2017]
  Update the policy with a trust-region policy gradient method
  In each iteration projects the policy to a safe feasibility set
  Meet safety constraints in expectation
Safe Exploration in Continuous Action Spaces [Dalal et al. 2018] (for this project)
  Propose a linearly approximated Safety Layer to predict the “safety signal”
  Closed form solution and simple implementation
  Tested on simple games and achieved zero safety violations
State of the Art – Safe Reinforcement Learning

## Slide 5
Learning to Drive in A Day [Kendall et al. 2018]
  First end-to-end application of deep RL in autonomous drive
  Variational auto-encoder (VAE) to extract the image features  fast training
  Practical implementation with Donkey Car simulator [Raffin & Sokolkov, github, 2019]
State of the Art – Autonomous Drive using RL

## Slide 6
Safe Exploration in Continuous Action Spaces [Dalal et al. 2018]
  Linear approximation to describe the safety signal with a neural network g(s,w)
  Revise the proposed action not to violate the safety constraint
  Close form solution available
State of the Art – Safety Layer method

## Slide 7
Case One: Simple Environment
  Most of the lane is straight, with very infrequent smooth turns
  Safety signal (the car’s max deviation off the lane) information collected by random sampling and running partially trained model
  The linearly approximated safety layer trained with two fully connected layers, with 64 and 16 neurons respectively
Implementation – Case One with Simple Environment
Lane Environment Front Camera Image

## Slide 8
Case One: Results – Gif Images
  The safety layer would push the car back to the lane when it is about to violate the boundary, thus safety is ensured
Implementation – Case One with Simple Environment
Without Safety Layer With Safety Layer

## Slide 9
Case One: Results
  Many safety violations at the initial training stage without the Safety Layer
  Zero safety violations at the initial training stage with the Safety Layer
  Positive lambda’s at the beginning shows the effect of the Safety Layer
Implementation – Case One with Simple Environment
Discounted reward Number of Safety Violations Value of Lambda

## Slide 10
Case Two: Complex Environment
  Many continuous sharp turns with almost no straight lanes
  Safety related information collected by random sampling and running well trained model
  The linearly approximated safety layer trained with two fully connected layers, with 64 and 16 neurons respectively
Implementation – Case Two with Complex Environment
Lane Environment Front Camera Image

## Slide 11
Case Two: Results – Gif Image
  The Safety-Layer push back is not enough for the car to go through the sharp turn
Implementation – Case Two with Complex Environment
With Safety Layer Sharp Turn Schematic

## Slide 12
Case Two: Results
  The training process with Safety Layer still has many safety violations, although slightly fewer than the case without Safety Layer
Implementation – Case Two with Complex Environment
Discounted reward Number of Safety Violations

## Slide 13
Higher order approximation might be needed for complex Environment
  Quadratic approximation to describe the safety signal with neural networks
  Revise the proposed action: quadratically constraint quadratic programming (QCQP)
  No close form solution available for QCQP
    Use suggest-and-improve heuristics to solve approximately [Park & Boyd, 2017]
    When the problem is not solvable, use the originally proposed action
Implementation – Case Two with Complex Environment

## Slide 14
Case Two: Results with quadratic approximation for safety signal
  The quadratic approximation gives even worse results concerning safety violations
  Possibly caused by QCQP not always solvable
Implementation – Case Two with Complex Environment
Discounted reward Number of Safety Violations

## Slide 15
Summary
Implemented the Safety Layer approach to ensure safety for reinforcement learning applied to autonomous drive
  Linear approximated safety layer works to some extent for simple environment
  Linear approximated safety layer does not work well for complex environment
  Quadratic approximated safety layer is proposed, and works badly for complex environment
Things to be considered for safe reinforcement learning with autonomous drive
  Concerning safety layer approach, it is necessary to collect safety signal data representatively and comprehensively
  More effort should be put into reinforcement learning algorithms, such as reward function design, policy optimization and so on